## Slide 1
1
INFRASURE · RISK PLATFORM · VALIDATION
How We Validate
Methodology and results — two questions, and how we answer each
Is the method sound, and are the numbers right? How we validate across the platform — hazard and damage, the CONUS grid and per-asset dollars — including range validation where no competitor number exists.
methodology
results
hazard grid
per-asset $
range validation
Internal — modeling & leadership

## Slide 2
2
VALIDATION, AT THE TOP LEVEL
Two questions — and they need different answers
1
IS THE METHOD SOUND?
Methodology validation
Is the approach itself defensible — the grain, the axis, the curve shape, the reasoning — and is every decision backed by a source? Answered per hazard × asset pair, in writing.
2
ARE THE NUMBERS RIGHT?
Result validation
Do the actual outputs hold up — the hazard grid and the per-asset dollars? Checked against independent data, competitor outputs, and credible reference ranges. This is the heavier half.
InfraSure · How We Validate · Internal
validation taxonomy · data & modeling framework sync 2026-06-25

## Slide 3
3
THE WHOLE PICTURE ON ONE SLIDE
The validation map
Two branches; results split by our two product outputs. This is the map for the rest of the deck.
METHODOLOGY VALIDATION
RESULT VALIDATION
is the method sound?
are the numbers right?
Hazard methodology
what we do per hazard × asset pair — 3 hazards built E2E
✓ built
Damage methodology
the worked-reference docs — hail · flood
✓ built
Adaptation & Resiliency
the Phase-3 arc, within damage — turning the curve's knobs
coming soon
Hazard results
the CONUS corners-level grid
QC + vs open-source & competitor
Financial results
per-asset dollars = hazard × damage
competitor, else range validation
Result validation is the heavier half — and where range validation earns its place.
InfraSure · How We Validate · Internal
validation taxonomy

## Slide 4
4
WHAT WE ARE VALIDATING
Where the two outputs come from
Validation targets the two things we ship. Both are built from the same pipeline — hazard coupled with the damage curve.
HAZARD
M0 → M1 → M2 → M3 → M4
DAMAGE CURVE
intensity → damage ratio
ASSET LOSS
per-asset loss distribution
OUTPUT 1 · Hazard grid
CONUS corners-level grid data — hazard intensity & risk metrics per grid cell, nationwide.
validated as a grid product
OUTPUT 2 · Per-asset financials
Per-asset detailed financial numbers — EAL / PML / return-period loss for a specific project.
validated as a dollar figure
InfraSure · How We Validate · Internal
Hazard_modeling M0→M4 · damage_modeling damage_code()

## Slide 5
5
BRANCH 1 · METHODOLOGY VALIDATION
Two layers: the generic method, then its implementation
Methodology validation isn't one thing. There's the generic method — defined once, a pre-step done anyway — and the implementation: the actual step-by-step we run for a specific hazard × asset pair.
LAYER 1 · Generic methodology
the pre-step — defined once, applies to every pair
the high-level M0 → M4 hazard framework
the generic damage build method (the 7 stages)
the general approach & principles — not pair-specific
necessary, and done anyway — but not sufficient on its own
applied to
LAYER 2 · Implementation methodology
per hazard × asset pair — the actual step-by-step
exactly what we do for THIS pair: grain, axis, form, params
every decision mapped to a source / evidence link
this is what the worked-reference documents ARE
where the method is really validated & made auditable
Generic methodology is the pre-step we do before any pair; implementation methodology is the per-pair record this deck's worked-reference docs deliver.
InfraSure · How We Validate · Internal
generic vs implementation methodology

## Slide 6
6
BRANCH 1 · IMPLEMENTATION METHODOLOGY
Implementation coverage — per hazard × asset pair
One worked-reference build per domain. Hazard and damage are in place; adaptation & resiliency is next.
HAZARD
methodology
✓ built
M0 → M4 per pair, 3 hazards built end-to-end (hail · wildfire · convective wind); catalog, coupling, intensity and metric choices — sourced.
DAMAGE
methodology
✓ built
The 7-stage worked docs (hail · flood); every decision + the curve-shape choice referenced; caveats & placeholders flagged with update triggers.
ADAPTATION & RESILIENCY
methodology
coming soon
Within the damage arc (Phase 3): turning the curve's exposed knobs — stow, feather, hardening, elevation — and pricing the trade-off.
Adaptation & Resiliency sits within the damage methodology (it adjusts the curve rather than adding a new engine).
InfraSure · How We Validate · Internal
Hail_Solar / Flood_Solar Worked Reference · Hazard_modeling notebooks · A&R (Phase 3)

## Slide 7
7
BRANCH 2 · RESULT VALIDATION
Two outputs, two kinds of validation
The grid and the dollar figure fail in different ways, so they are checked differently.
TRACK 1 · Hazard results
The CONUS grid — a hazard comparison
quality-control + statistical checks on the grid
compare spatial pattern vs open-source climatology / source products
compare vs competitor hazard outputs where available
the raw hazard layer — before dollars
TRACK 2 · Financial results
Per-asset dollars — hazard × damage combined
the number that actually matters to a client
compare to a competitor number IF one exists at this granularity
usually none is available per-asset → range validation
combines both engines, so it validates them jointly
InfraSure · How We Validate · Internal
result validation

## Slide 8
8
TRACK 1 · HAZARD RESULTS
Validating the grid — QC, then competitor comparison
Two moves: the grid must be internally sound (quality control), then it is compared to independent products on standard metrics.
1
Quality control & statistical checks
grid-join integrity — events/pixels hit the right cell
coverage — no-data is never treated as zero risk
plausibility vs climatology (external anchor)
point-vs-cell consistency with deep asset runs
metric identity + tail caveats on sparse cells
the six QC families → Appendix A
2
Competitor / similar-product comparison
Compare the grid to open-source climatology and competitor hazard layers using standard metrics:
spatial correlation vs source product
mean bias & RMSE against independent estimates
POD / FAR — hit rate & false-alarm for event detection
return-period / quantile agreement (1-in-T)
PLACEHOLDER — Track 1 deep-dive coming. This track will get its own detailed slides — per-hazard QC metrics, competitor-comparison plots, and standard-metric tables — to document Track 1 at the same depth as Track 2 (which follows). Held here intentionally so the structure is visible now.
InfraSure · How We Validate · Internal
Hazard_modeling docs/plans/hazard_conus_grid/common/validation.md

## Slide 9
9
TRACK 2 · FINANCIAL RESULTS
No competitor number? Validate the range
The per-asset dollar figure is the hard case: at this granularity a comparable competitor number rarely exists.
Our per-asset $
EAL · PML · return-period loss for a specific project
Is there a competitor number at THIS granularity?
YES — compare directly
rare per-asset; use it when it exists
NO — range validation
check the number lands inside a credible envelope of reference values
Why range, not a point
there is no single “true” loss number for one asset-year
reference numbers are gross/net- and basis-inconsistent
a defensible band is honest; a false-precision match is not
InfraSure · How We Validate · Internal
renewable_loss_benchmark_source_library v0.2

## Slide 10
10
TRACK 2 · THE METHOD
Range validation — a credible envelope, not a target
We assemble renewable-specific reference numbers into an envelope, then check our output falls inside it. A renewable-first evidence hierarchy keeps generic property data from leading.
R1
Renewable claims / loss databases with actual $
kWh, AXIS, GCube, Marsh
R2
Renewable-specific engineered PML / AAL / cat-model
VDE, Renew Risk, Moody's RMS
R3
Renewable event case studies & forensic reports
Midway, Fighting Jays, J.S. Held
R4
Renewable engineering studies w/ financial implications
DOE/FEMP, PVEL/Kiwa, RETC
R5
Generic public hazard/loss data — secondary context only
NOAA, FEMA NRI
Renewable-first: generic real-estate loss data never leads the benchmark unless no renewable path exists — and then the limit is stated.
InfraSure · How We Validate · Internal
renewable_loss_reference_source_pathways.md §2

## Slide 11
11
TRACK 2 · BUILDING THE RANGE
No one hands you a range — we reverse-engineer one
No source publishes “US solar-hail loss is $X–$Y.” Reports give losses for a specific asset or asset type. We turn those into a comparable envelope using our own per-asset financial breakdowns.
1
Collect what reports actually give
per-asset / per-type event losses — $/MW, $/claim, event totals — never a national range
2
Classify the loss basis — orange to orange
what does “loss” mean here: physical damage, overall, or business interruption? strip to a like-for-like basis before comparing
3
Recast to a common denominator
use our per-asset financial breakdown (component × $ + capacity) → %TIV, % module value, implied DR
4
Assemble the envelope & check
the normalized anchors define a credible band; confirm our per-asset output lands inside
Our engine
Per-asset financial breakdown
for every U.S. solar asset: capacity (MW) + a component-level dollar breakdown
yields value buckets: TIV · physical · module · module + fieldwork
converts any raw $ number into %TIV and an implied damage ratio
same breakdown that drives our output — so both sides share a denominator
InfraSure · How We Validate · Internal
solar_hail_value_damage_crosswalk.md · per-asset value ledger

## Slide 12
12
TRACK 2 · WORKED EXAMPLE — SOLAR × HAIL
Does our number land in the credible range?
Illustrative: a fixed-tilt, no-stow per-asset severity (≈27% of installed TIV) sits inside the envelope from AXIS's 5-yr claims. Normalizing to %TIV — not raw $ — is what makes it a like-for-like check.
Corroborating anchors
73%
hail = share of solar loss $ (kWh SRA 2025)
$58.4M
avg hail claim; 54% of hail loss cost (GCube)
$70–80M
Midway Solar event (178 MW, 2019)
$50M
Fighting Jays hail sublimit (2024)
PML / AAL
VDE engineered hail loss, per site
InfraSure · How We Validate · Internal
benchmark_number_matrix_solar_hail · AXIS/GCube/kWh/VDE (see appendix)

## Slide 13
13
TRACK 2 · MAKING NUMBERS COMPARABLE
The value / damage crosswalk — normalize before you compare
We recast both sides onto our value buckets (from the per-asset breakdown), so a raw $/MW becomes a comparable %TIV and maps to the grain our curve actually damages.
Our value buckets ($/MWdc · % TIV)
Installed TIV
$1.12M
100%
Physical replaceable
$878k
78%
Module hardware (M3 unit)
$291k
26%
Module + fieldwork
$398k
36%
Module hardware is the grain our M3 hail curve actually damages.
AXIS severity, recast onto our buckets
Successful stow
$150k
13% TIV
fits module bucket
Fixed-tilt
$340k
30% TIV
needs fieldwork / claim
Failed stow
$380k
34% TIV
needs fieldwork / claim
Gross claim $ above module value is not a curve error — it usually includes fieldwork / claim costs. Classify the loss basis first.
InfraSure · How We Validate · Internal
02_crosswalks/solar_hail_value_damage_crosswalk.md §2–3

## Slide 14
14
TRACK 2 · HONEST FRAMING
What range validation is — and is not
It IS
a plausibility envelope — does the number sit where credible evidence says it should?
a defense against silent 10× errors
basis-aware — normalized before comparison
honest about gross vs net, BI inclusion, portfolio bias
It is NOT
calibration — it does not fit parameters to the references
a pass/fail on a single “true” number
a claim that competitor / commercial numbers are ground truth (most are gated & portfolio-biased)
a substitute for claims calibration once real loss data arrives
InfraSure · How We Validate · Internal
renewable_loss_reference_source_pathways.md §0

## Slide 15
15
WHERE EACH PIECE STANDS
Validation status & roadmap
Hazard methodology
Implementation per pair; 3 hazards built E2E
done
Damage methodology
Worked-reference docs, hail & flood
done
Adaptation & Resiliency
Within damage (Phase 3) — knobs & trade-off
coming soon
Hazard results (Track 1)
QC in place; competitor-metric slides to add
in place · deepening
Financial — range validation
Source library v0.2 built for solar × hail
v0.2 · expanding
Next pairs
flood, strong wind, wildfire
queued
InfraSure · How We Validate · Internal
validation status · 2026

## Slide 16
16
WHAT TO HOLD ONTO
Five things
1
Two questions — is the method sound (methodology) and are the numbers right (results).
2
Results split by output — the CONUS hazard grid and the per-asset dollar figure are validated differently.
3
Hazard grid → comparison — QC + climatology + competitor outputs, via six validation families.
4
Financial → range validation — no per-asset competitor number, so we check a credible reference envelope.
5
Honesty is the point — a defensible band beats false precision; every basis and caveat is named.
Read next: the hail & flood worked-reference docs · hazard_conus_grid/validation.md · renewable_loss_benchmark_source_library

## Slide 17
17
APPENDIX A
Hazard grid validation families — detail
Family
What it checks
Applies to
Grid join
source pixels/events attach to the intended cell_id; no key drift
all hazards
Coverage
no-data is not treated as zero risk
all hazards
External anchor
broad spatial pattern agrees with independent climatology / source product
all hazards
Point-vs-cell
known assets/cells behave consistently with deep asset notebooks
all hazards
Metric identity
PML_T = VaR_(1−1/T); AEP / OEP frames do not mix
risk layer
Tail caveat
sparse / short-record cells and bootstrap-limited tails are flagged
risk layer
Hail first-checks: MRMS severe-hail-day counts plausible; MESH marked radar-estimated (not ground truth); Storm Events agrees directionally; sparse cells flagged before fitting tails.
InfraSure · How We Validate · Internal
Hazard_modeling docs/plans/hazard_conus_grid/common/validation.md

## Slide 18
18
APPENDIX B
Range-validation source tags
Every reference source is tagged so its role is explicit and it is never over-claimed.
Availability
HAS_OPEN_NUMBERS
usable public values
HAS_GATED_NUMBERS
behind report/API/paywall
HAS_PATHWAY_ONLY
owner exists; needs outreach
GENERIC_ONLY
not renewable-specific
Metric type
CLAIM_SEVERITY
$/claim or $/MW
PERCENT_TIV
% of insured/asset value
AAL / PML
annual avg / return-period loss
EVENT_LOSS
named-event amount
Caveat
GROSS_VS_NET_UNKNOWN
loss basis unclear
BI_INCLUDED_UNKNOWN
downtime in/out?
TIV_BASIS_UNKNOWN
which denominator?
PORTFOLIO_BIAS
one insurer's book
Evidence-use tags (PRIMARY_BENCHMARK_CANDIDATE · SECONDARY_BENCHMARK · CASE_STUDY_ONLY · MECHANISM_ONLY · DENOMINATOR_ONLY) decide whether a source can anchor a range or only support one.
InfraSure · How We Validate · Internal
renewable_loss_reference_source_pathways.md §1

## Slide 19
19
APPENDIX C
Solar × hail benchmark anchors
Source
Number
Type
Tier
kWh SRA 2025
hail = 73% of solar loss $ (6% of incidents)
CLAIM_SHARE
R1
AXIS 2025
55% of gross NatCat $; $150/340/380k/MW by stow
CLAIM_SEVERITY
R1
GCube (Hail No!)
~$58.4M avg hail claim; 54% of hail cost
CLAIM_SEVERITY
R1
Midway Solar 2019
$70–80M event; ~400k modules; 178 MW
EVENT_LOSS
R3
Fighting Jays 2024
$50M hail sublimit exceeded (350 MW)
DEDUCTIBLE
R3
VDE Hail Risk
engineered PML / AAL, per site & return period
PML / AAL
R2
Full source registry, links, and the benchmark-number matrix live in renewable_loss_benchmark_source_library_v0_2 (data/ + 01_pairs/solar_hail).
InfraSure · How We Validate · Internal
01_pairs/solar_hail · source_registry_solar_hail.json