## Slide 1
1
INFRASURE · RISK PLATFORM · VULNERABILITY LAYER
Damage Modeling
From hazard intensity to a damage ratio
A from-the-basics walkthrough of the curve layer: what it is, why it earns its own home, the seven-stage build pipeline, and how it plugs cleanly into hazard modeling.
intensity → DR
per failure-unit
provenance-carried
versioned contract
Internal — modeling team

## Slide 2
2
THE ONE JOB
Turn a hazard intensity into a damage ratio
intensity x the asset's vulnerability → damage ratio DR ∈ [0, 1]
DR = repair cost ÷ replacement value — physical destruction only, per thing-that-fails.
What it is NOT
A whole-plant guess, a single literature curve, or a chart in a slide. It is a parameterized, callable function with a contract.
What rides with it
Every parameter maps to a source or a named assumption. Provenance is the deliverable, not an afterthought.
Where it stops
It emits a DR (and a capability declaration). It does not compute EAL, PML, or portfolio loss — that is the consumer's job.
InfraSure · Damage Modeling — From the Basics · Internal
docs/damage_curves/SCOPE_AND_STORY.md §1, §5 · AGENTS.md

## Slide 3
3
WHERE IT SITS IN THE PLATFORM
A shared substrate that feeds Hazard's M3 stage
Damage modeling is not a fourth risk tier. It is a substrate the Hazard tier consumes at one point — the M3 (damage) stage.
1 · PERFORMANCE
model-gpr — normal ops → P50 / P90 / P99
2 · HAZARD
M0 → M1 → M2 → [ M3 ] → M4 → asset loss · EAL · PML · VaR
3 · OVERALL
performance + hazard → Total Loss
M3 stops CONTAINING the curve and starts CONSUMING it.
DAMAGE MODELING
this repo
intensity → damage ratio
per failure-unit
provenance-carried
versioned curve packages
+ a damage_code() API
consumed at M3 only
InfraSure · Damage Modeling — From the Basics · Internal
docs/damage_curves/SCOPE_AND_STORY.md §3

## Slide 4
4
THE THREE-PHASE ARC
Damage was assumed → now it is built → then it is adjusted
PHASE 1
Hazard-first ("IDF")
M0→M4 engine stood up end-to-end using a few generic / borrowed damage curves.
damage = assumed
done
PHASE 2
Damage from the ground up
Build the curve properly: grain · axis · form · coverage · provenance · value-link · emit object.
damage = built
we are here
PHASE 3
Adaptation & resiliency
Turn the knobs the curve already exposes — stow, feather, hardening, elevation — and price the trade-off.
damage = adjusted
future
Phase 2 ↔ 3 is deliberately blurry: the resiliency levers already live in Phase 2 as conditioners / selectors / exposure modifiers. Phase 3 is evidence + magnitude on knobs the curve already has.
InfraSure · Damage Modeling — From the Basics · Internal
docs/damage_curves/SCOPE_AND_STORY.md §2, §8

## Slide 5
5
WHY WE MODEL AT THE FAILURE-UNIT
One cell can be one curve — or many
The grain isn't a style choice. Different hazards concentrate damage differently, so the same asset needs a different number of curves depending on the hazard.
HAIL × SOLAR
Damage collapses onto essentially one thing
PV module glass / cell
  primary-nonzero — carries the curve
mounting / inverter / racking / substation
  reviewed, tagged DR ≈ 0 for direct hail
⇒ one primary curve drives the cell
FLOOD × SOLAR
Damage spreads across many local-exposure units
inverter · switchgear · transformer controls
combiner / DC protection · SCADA cabinets
cable / conduit · foundation scour · modules
each has its own datum & replacement logic
⇒ a family of curves, composed by summation
InfraSure · Damage Modeling — From the Basics · Internal
01_cells/hail_solar · 01_cells/flood_solar (README v1)

## Slide 6
6
THE BUILD PIPELINE
Seven stages, in strict order
Each stage has one decisive question, one input, one output. The order is forced: you can't choose the form before the axis, or the axis before the grain.
1
EVIDENCE
What does the curated base authorize the curve to claim?
2
GRAIN
At what level is a curve written — and how do levels compose?
3
AXIS
What variable indexes damage for each failure-unit?
4
FORM
What shape does the curve take, and where are its anchors?
5
ADJUSTMENTS
What does it depend on besides intensity, and how?
6
EMIT
What does it return per event — and the capability declaration?
7
SHIP
What does the consumer receive, and on what terms?
Collapsing stages hides decisions; splitting them creates sub-stages that share doctrine with their parent. Seven is the minimal honest set.
InfraSure · Damage Modeling — From the Basics · Internal
damage_curve_build_methodology.docx §3

## Slide 7
7
1
STAGE 1 EVIDENCE
What does the curated evidence base authorize the curve to claim?
Four evidence tiers — graded per claim
T1
Direct empirical
loss observed on the actual asset × hazard, intensity recorded
T2
Engineering standards
consensus standards & lab tests — IEC, IBHS, ASCE, HAZUS
T3
Inferred / proxy
related-but-not-identical asset, hazard, or scale
T4
Expert judgment
documented opinion / OEM notes — not test reports
The binding rules
Curated, not fitted — every parameter is attributed to an artifact; the optimizer does not override the curation.
Tier per claim — a 2024 paper is T1 for what it tested, T3 for adjacent claims — never graded in the abstract.
No silent demotion — mixing a T1 paper with a T3 proxy in one fit quietly demotes the T1. Don't.
A found curve is just an artifact — never copied as a black box — decomposed into anchors and re-derived.
The weakest-tier parameter gates which metrics are honest downstream.
InfraSure · Damage Modeling — From the Basics · Internal
damage_curve_build_methodology.docx §4 · damage_curve_evidence_reference.docx

## Slide 8
8
2
STAGE 2 GRAIN
At what level is a curve written — and how do those levels compose?
The composition rule
cell_DR = Σ ( capex_shareᵢ × unit_DRᵢ )
Capex-weighted summation, each unit's DR capped at its own saturation. No grouping primitive — composition is always explicit, so double-counting can't hide.
Worked split — hail × solar (illustrative):
panel_glass 0.65
mounting/tracker 0.20 · inverter 0.10 · racking 0.05
The doctrine
Subsystem-default — write at panel-glass / inverter / racking level — not panel-as-monolith.
Finer where mechanism concentrates — split only where evidence supports a separate curve.
Role assigns the effort — primaries get the evidence & care; secondaries get standards shapes; conditioner-only / exposure units carry no curve.
Immune ≠ ignored — DR≈0 parts are kept as explicit reviewed records, not dropped.
InfraSure · Damage Modeling — From the Basics · Internal
damage_curve_build_methodology.docx §5 · questions/01_granularity.md

## Slide 9
9
3
STAGE 3 AXIS
What variable indexes damage for each failure-unit?
Why it earns its own stage: the indexing variable isn’t given — it’s an evidence-driven choice. Different reports measure damage against different variables, and it’s rarely the one the hazard catalog reports. Pick the variable that actually drives the failure. (Hail is the easy case: just diameter.)
The chain-position rule — index by what HITS the unit, not what the hazard reports
Radar reflectivity
hazard catalog reports
MESH → diameter
M3 chain conversion
Hail diameter (mm)
what hits the panel — THE AXIS
Physical units, always
wind m/s · hail mm · ground motion g · depth m · flux kW/m². Never normalized, never dimensionless.
Valid range, declared
outside it the curve does not extrapolate — the emit is undefined, not a best guess.
Univariate in v1
one axis per unit; a second dependency becomes a conditioner. Multivariate is a major-version event.
InfraSure · Damage Modeling — From the Basics · Internal
damage_curve_build_methodology.docx §6 · questions/02_x_axis_intensity_variable.md

## Slide 10
10
4
STAGE 4 FORM
What shape does the curve take, and where are its anchors?
Anchored logistic — hail × solar default module (real v1.0 parameters)
Curve forms — logistic is the default, not the only option
DR(x) = L / (1 + e^(−k(x − x₀)))
Logistic
default · smooth onset → cap · 3 params
Piecewise-linear
evidence reports sharp damage-state jumps
State-based (fragility)
evidence is in states; consumer wants P(state)
PCHIP (monotone cubic)
dense anchors; smooth, monotone interpolation
Linear
only a slope between two anchors
Whatever the form: anchor the onset · cap at L · no extrapolation past the valid range.
InfraSure · Damage Modeling — From the Basics · Internal
damage_curve_build_methodology.docx §7 · hail_solar curve_artifact.json

## Slide 11
11
5
STAGE 5 ADJUSTMENTS
What does the curve depend on besides intensity — and how does each enter?
SELECTOR
picks the curve
fixed asset attribute, set at bind-time
e.g. module archetype / glass type
CONDITIONER
adjusts the curve
event-time state, recomputed per event
e.g. tracker stow when the storm arrives
EXPOSURE
scales to dollars
value-share touched, set at bind-time
e.g. array exposure fraction
Selector in action: three module archetypes are three shifted curves — the selector chooses which family applies.
Caveat — exposure is a v2 item. Partial / footprint exposure (f < 1) is in the contract but not yet exercised in the hazard-modeling integration. Today it runs at full site (f = 1.0).
InfraSure · Damage Modeling — From the Basics · Internal
damage_curve_build_methodology.docx §8 · questions/… selector_conditioner_exposure

## Slide 12
12
6
STAGE 6 EMIT
What does the curve return per event — and what capability ships with it?
The emit shape is chosen by the FIRST NONLINEARITY downstream the curve must honor.
scalar mean DR
triggered by
linear functional (EAL)
sufficient when the consumer integrates a linear functional of DR
mean + spread
triggered by
a deductible / limit
needed once a nonlinear financial term bites the distribution
state vector
triggered by
state-conditioned repair
when the consumer applies damage-state repair logic
full distribution
triggered by
tail quantiles (PML, VaR)
required to honestly produce deep-tail metrics
Withhold, not caveat.
A scalar curve over the event set still gives an honest expected loss — what it drops is within-event spread, which dominates the deep tail. So a scalar tail would be understated; the curve withholds it rather than shipping it wrong. The consumer literally cannot emit a withheld metric.
InfraSure · Damage Modeling — From the Basics · Internal
damage_curve_build_methodology.docx §9 · questions/06_metrics_and_tail_honesty.md

## Slide 13
13
WORKED EXAMPLE · HOW THE CURVE IS ACTUALLY BUILT
Hail × solar (1) — the question comes before the math
STEP 0 · we are NOT asking
hail size → whole-plant loss %
STEP 0 · we ARE asking
hail diameter (mm) → PV module glass / cell DR
Core failure unit: PV_MODULE_GLASS_CELL — hail breaks the exposed module glass/cells; inverters, racking, civil are reviewed but stay DR ≈ 0 in v1 unless a direct-hail mechanism is shown.
The evidence we go looking for — and the role each plays
1
NOAA Storm Events / MESH → fixes the x-axis: hail diameter in mm — not energy, not return period
2
IEC / DOE-FEMP hail test → the near-zero boundary: a qualified module ≈ 1% DR at 25 mm
3
PVEL / Kiwa lab breakage → the curve-shape anchors — real breakage % at each hail size
4
Field / claims (NREL, VU Amsterdam) → validation & caveats only — not refit into v1 curves
The anchors it produces
Archetype
anchors (mm → DR)
Default 3.2 GBS
25→1% · 50→39%
Fragile glass-glass
35→18% · 45→61% · 50→89%
Hardened thicker
25→0.5% · 45→7%
IEC is read as a boundary, not a loss curve: a qualified module shows very low DR near 25 mm — not a literal 0%.
InfraSure · Damage Modeling — From the Basics · Internal
hail_solar_curve_derivation_dossier_v1_3.md · 00_curve_curation_walkthrough.ipynb

## Slide 14
14
WORKED EXAMPLE · HOW THE CURVE IS ACTUALLY BUILT
Hail × solar (2) — fit, select, condition, value
The logistic fit, drawn through the real anchor points — three module archetypes, three curves.
FIT
Fit a logistic in logit space from the anchors → D50 (half-damage size) and k (steepness) per archetype.
SELECT
Selector module_archetype picks which curve — fixed asset metadata (glass type, thickness, rating).
CONDITION
Conditioner stow_state blends at event time: DR = P·0.90·logistic(D50+8) + (1−P)·logistic(D50).
Source: VDE Americas hail-stow memo · DOE/FEMP hail mitigation — direction only; the +8 mm / ×0.90 magnitude is a T4 placeholder.
VALUE
loss = DR × exposure_fraction × module value — never applied to the whole-plant TIV.
The whole flow: define failure unit → axis evidence → standards boundary → lab anchors → field as caveats → fit logistic → selector → stow conditioner → keep value separate → ship JSON
InfraSure · Damage Modeling — From the Basics · Internal
hail_solar__model_v1_0 curve_artifact.json · derivation dossier v1.3

## Slide 15
15
WORKED CONTRAST — WHY THE METHOD GENERALISES
Flood × solar: many failure-units, a different curve form
Flood equipment damage is threshold-like, indexed by local depth above each component's critical elevation — so the form is piecewise / state, not logistic.
What changes vs. hail × solar
Grain
many primary units — inverter, switchgear, transformer controls, combiner, SCADA
Axis
local water depth above each component datum (+ a velocity/scour proxy)
Form
piecewise-linear / state — water is in, or it isn't
Exposure f
site geometry & elevation, not material / BOM share
Same pipeline, same contract — the grain, axis, and form just resolve differently for the hazard. That portability is the whole point.
InfraSure · Damage Modeling — From the Basics · Internal
01_cells/flood_solar/current (README v1.0)

## Slide 16
16
THE HONEST STATE OF THE WORK
Method is mature; evidence is young — and that's managed
Method (new work)
Deep & right — keep all of it
CELL → failure-unit architecture
coverage roles
provenance discipline
emit / tail-honesty resolution
Evidence (new work)
Young — public-derived, not claims-calibrated
all 3 cells public-source-derived
load-bearing placeholders
  hail stow +8 mm (T4)
  flood scour proxy; wind D50/k partly one case
The bridge
Standard 16 — reference ingestion
Absorb the old repo's strong evidence the right way: intake → triage → axis-compatibility → source-to-parameter map → impact → version bump.
Method from the new work; evidence from the old. A maturity badge travels with every runtime curve.
InfraSure · Damage Modeling — From the Basics · Internal
docs/damage_curves/SCOPE_AND_STORY.md §7 · standard 16

## Slide 17
17
THE FIVE THINGS TO HOLD ONTO
If you remember nothing else
1
A curve is a callable, not a chart — parameterized, provenance-carried, with a capability declaration.
2
We model at the failure-unit — then assemble by capex-weighted summation — sum, don't group.
3
Build in strict order — EVIDENCE → GRAIN → AXIS → FORM → ADJUSTMENTS → EMIT → SHIP.
4
We declare; the consumer computes — damage owns DR + capability; hazard owns EAL / PML / portfolio.
5
Honesty is the feature — weakest tier gates metrics; withhold, don't caveat; flag every open seam.
Read next: SCOPE_AND_STORY.md · the build methodology doc · the notebooks (hail/solar, flood/solar)

## Slide 18
18
APPENDIX A
Evidence tiers — graded per claim, weakest gates the metric
Tier
Name
What it means
Examples
T1
Direct empirical
Loss observed on the actual asset × hazard with intensity recorded
attributed claims, field campaigns, realistic test stands
T2
Engineering standards
Consensus standards and lab tests
IEC, IBHS, ASCE, HAZUS
T3
Inferred / proxy
A related-but-not-identical asset, hazard, or scale
coupon tests, cross-event transfer
T4
Expert judgment
Documented credentialed opinion or OEM notes that aren't test reports
vendor engineering notes
A tier grades an artifact for the specific claim being made — not in the abstract. The same paper can be T1 for its own specimen and T3 transferred to another asset.
InfraSure · Damage Modeling — From the Basics · Internal
damage_curve_evidence_reference.docx · §2.2 of build methodology

## Slide 19
19
APPENDIX C
Glossary — the words this deck assumes
Damage curve
A callable: a parameterized function + capability declaration. Not a chart.
Failure-unit
The level a curve is written at — the damage-code atom (e.g. panel glass).
Cell
A (hazard × asset) pair; ships a family of curves, one per failure-unit.
Selector
Fixed asset attribute that picks a curve variant (bind-time).
Conditioner
Event-time state that adjusts parameters (e.g. stow angle).
Exposure
The value-share a failure-unit touches; scales DR into dollars.
Emit object
What the curve returns per event: scalar, mean+spread, state, or distribution.
Capability declaration
Metadata saying which downstream metrics the curve honestly supports.
Damage ratio (DR)
Repair cost ÷ replacement value, in [0, 1] — physical destruction only.
Cap-binding preflight
The check that gates a scalar EAL: confirms the cap rarely binds.
InfraSure · Damage Modeling — From the Basics · Internal
damage_modeling_terminology.docx